INSTRUCTIONS

The DM-1 can be configured in a variety of ways, depending upon your needs. Typically, the IN line (line 1) is connected to the source(tap) water, and the OUT line (line 2) is connected to the product (filtered) water. The DM-1 can also be configured whith multiple systems, such as an RO/DI combination, as well as with HM Digital's Single Inline TDS Monitor (model SM-1).

Installation

To install DM-1 to a water purification or filtration system:

- Insert the white sensors fully into the bottom of the T-fittings.

- Orient the sensor pins so that they are perpendicular to the direction of the T. The water should flow over both pins equally. (You should be able to see both pins of you look through the fitting.) See illustration #1 below.

- Disconnect the water source.

- Snip the source (tap) water tube at a point between the source and the filter. Instert both ends od the tube into the top of teh IN line sensor's T-fitting. See illustration #2.

- Snip the product (filtered) water tube at a point between the filter and a dispenser. Insert both ends of the tube into the top of the OUT line sensor's T-fitting. See illustration #2.

- The DM-1 monitor can be attached anywhere on or near the water system using the Velcro tape. Most commonly, the monitor is attached to the water filter system.

- Reconnect the water source. Your monitor is now redy to use.

- NOTE: Consult a professional plumber for specific installation questions

INSTALACJA

Aby zainstalować DM-1 do systemu filtracyjnego lub oczyszczającego wodę:

- Należy włożyć białe czujniki do dołu trójników.

- Należy ustawić czujniki prostopadle do kierunku przepływu wody w trójniku. Woda powinna przepływać przez czujniki jednakowo. (Powinieneś być w stanie zobaczyć oba piny patrząc poprzez trójnik).

- Należy odłączyć źródło wody.

- Jeden trójnik zamontuj pomiędzy źródłem wody a systemem filtracyjnym a drugi trójnik pomiędzy filtrem a dozownikiem.

- DM-1 może być umieszczony w dowolnym miejscu, jednak najczęściej jest umieszczany za pomocą taśma Velcro (znajdującym się na tylnej części urządzenia) na urządzeniu filtracyjnym.

- Podłącz źródło wody, urządzenie jest gotowe do użycia.